GOVERNMENT OF THE PEOPLE’S REPUBLIC OF BANGLADESH

OFFICE OF THE EXECUTIVE ENGINEER

Khulna PWD DIVISION-1

Khulna.

Corrigendum Tender Notice

Memo No. 3583                                                                                                                                                              Date: 16-08-2016

It is to inform to all concerned that the invitation for Tenders, 01(E/M)/2016-2017 “Supplying and Installation of 2(two) Nos. Passenger Lift( 800 kg. 8 stops) at RAB-6 Complex , Khulna under “Construction of 7(seven)RAB Complex” project one at Khulna.

| Sl. no | Description of Items | As Per Tender Notice | As Per Corrigendum Tender Notice |
| --- | --- | --- | --- |
| 01. | Schedule of Requirements | Supply of Passenger lift complete with car, control panels, driving motor, gear box/gear less, steel suspension ropes, safety devices, guide rails, push buttons, architraves (as required) with other necessary accessories etc. complete including counter weight made of cast iron as required, suitable for installation & use in tropicalised country like Bangladesh & as per detailed specification and standard as mentioned below: Detailed specification of Lift i) Capacity 800 kg( 10 passengers) ii) No.of stop: 8(Eight stops) iii) Speed : 1.5 meters per second iv) Car Travel height: 30 Meters ( Approximate) v)Floor Designations: G, 1,2,3,4,5,6,7 vi) Car Dimension: wide 1350 mm Depth 1400mm vii) Power rating : Compatible with capacity of the lift as mentioned above with 180 starts per hour minimum | Supply of Passenger lift complete with car, control panels, driving motor, gear box/gear less, steel suspension ropes, safety devices, guide rails, push buttons, architraves (as required) with other necessary accessories etc. complete including counter weight made of cast iron as required, suitable for installation & use in tropicalised country like Bangladesh & as per detailed specification and standard as mentioned below: Detailed specification of Lift i) Capacity 800 kg( 10 passengers) ii) No.of stop: 8(Eight stops) iii) Speed : 1.0 meter per second iv) Car Travel height: 30 Meters ( Approximate) v)Floor Designations: G, 1,2,3,4,5,6,7 vi) Car Dimension: wide 1350 mm Depth 1400mm vii) Power rating : Compatible with capacity of the lift as mentioned above with 180 starts per hour minimum |

All other terms & conditions of the tender will remain unchanged. This corrigendum notice will be part & parcel of the tender.

Muhammad Jakir Hossain

Executive Engineer

Khulna PWD Division-1

Khulna.